## Slide 1: Layered Comms Profile in SysML v1
Orientation – Tour - Examples

## Slide 2: SPDX Info
For this presentation
SPDX-License-Identifier: CC-BY-4.0
SPDX-FileCopyrightText: Copyright 2026 Guy Meador
SPDX-FileType: DOCUMENTATION
The MeadorTech logo(s) are trademarks of Meador Technologies, LLC, are used by special permission, and are not licensed as a part of this document or the licenses identified on this page. Derivative works are not authorized or licensed to use these logos.
Other Copyrights as noted on individual slides
For any SysML representations
SPDX-License-Identifier: Apache-2.0
SPDX-FileCopyrightText: Copyright 2026 Guy Meador
SPDX-FileType: SysML

## Slide 3: Layered Protocols Primer

## Slide 4: OSI Model Summarized
The Open Systems Interconnection (OSI) model is a reference model developed by the International Organization for Standardization (ISO)
the components of a communication system are distinguished in seven abstraction layers
Data processing by two communicating OSI-compatible devices proceeds as follows:
The data to be transmitted is composed at the topmost layer of the transmitting device (layer N) into a protocol data unit (PDU).
The PDU is passed to layer N−1, where it is known as the service data unit (SDU).
At layer N−1 the SDU is concatenated with a header, a footer, or both, producing a layer N−1 PDU. It is then passed to layer N−2.
The process continues until reaching the lowermost level, from which the data is transmitted to the receiving device.
At the receiving device the data is passed from the lowest to the highest layer as a series of SDUs while being successively stripped from each layer's header or footer
until reaching the topmost layer, where the last of the data is consumed.
The information below is from Wikipedia page https://en.wikipedia.org/wiki/OSI_model that carries the following statement “Text is available under the Creative Commons Attribution-ShareAlike 4.0 License; additional terms may apply. By using this site, you agree to the Terms of Use and Privacy Policy. Wikipedia® is a registered trademark of the Wikimedia Foundation, Inc., a non-profit organization.”

## Slide 5: Key Concepts

## Slide 6: Key Concepts
Host 2
Host 1
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Hosts participating in a layered comms pattern
Each protocol is represented by a protocol entity in each host

## Slide 7: Key Concepts
Host 2
Host 1
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
SAP
SAP
SAP
SAP
SAP
SAP
SDUs
SDUs
SDUs
SDUs
Within each host, a protocol entity offers its services to other protocol entities via a Service Access Point (SAP)
Service Data Units are exchanged between protocol entities in the protocol stack on the host

## Slide 8: Key Concepts
Host 2
Host 1
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
SAP
SAP
SAP
SAP
SAP
SAP
SDUs
SDUs
SDUs
SDUs
SDU Link
SDU Link
SDU Link
SDU Link
SDU Links are the connector type between stacked protocol entities within a host
Protocol Entities in one layer depend on the services of one or more protocols in the next lower layer.

## Slide 9: Key Concepts
Host 2
Host 1
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
SAP
SAP
SAP
SAP
SAP
SAP
SDUs
SDUs
SDUs
SDUs
PDU Link
PDU Link
PDU Link
PDUs
PDUs
PDUs
SDU Link
SDU Link
SDU Link
SDU Link
Protocol entities in different hosts exchange Protocol Data Units (PDUs) of the protocol.
PDU Link is the connector type between such protocol entities

## Slide 10: Key Concepts
Host 2
Host 1
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
Protocol Entity
SAP
SAP
SAP
SAP
SAP
SAP
SDUs
SDUs
SDUs
SDUs
PDU Link
PDU Link
PDU Link
PDUs
PDUs
PDUs
SDU Link
SDU Link
SDU Link
SDU Link
PDU Ports
The PDU Link connector is between the PDU Ports on each Protocol Entity within a given protocol.
PDU Links of a protocol in one layer may depend on PDU Links of a protocol in the next lower layer
The «Over» relationship is used to represent this relationship (not shown).

## Slide 11: Layered Comms Profile in SysML v1
com.meadortech.LayeredCommsProfile

## Slide 12: Purpose
Provides a profile and library model elements to assist system model creation following the layered comms principles
Provides
  Stereotypes
  Building block model elements (ex. ProtocolEntity, PDUPort, SAP, etc.)
  A pre-fabricated protocol package (a.k.a. ”Pre-Fab”) to leverage for modeling a protocol
    Copy & paste into your user model and rename a few things
    Add protocol-specific aspects (ex. protocol state machine, other behaviors, specific PDU and SDU types, etc.)

## Slide 13: Provided Base Model Elements and Stereotypes
Abstract library elements to be specialized by user models defining new protocols.
Includes stereotypes also to be applied when using a defined protocol (and/or defining one).

## Slide 14: Protocol Entity Aspects
The pattern for protocol entities
Specific protocols defined in user models will specialize each of these elements
Stereotypes are used for many aspects of the pattern and should be applied consistently in user models
Interfaces have appropriate flow properties
Protocol Entities have a Protocol State Machine marked by a supplied stereotype
  Not the same as UML protocol state machine

## Slide 15: PDU Aspects
Protocol Data Units are exchanged by Protocol Entities on different hosts
  PDU based on SysML signal with «PDU» stereotype
PDULink types connectors between PDUPorts
  Represented as Association Blocks so internal structure and behavior can be added at need in the concrete protocol
  Also note «PDULink» stereotype should be applied
  Provides mechanism to assert compatibility between the interface types within a protocol
Specific protocols defined in user models will specialize each of these elements and apply the appropriate stereotypes for the pattern

## Slide 16: SDU Aspects
Service Data Units are exchanged by Protocol Entities on the same host participating in the protocol stack
  SDU based on SysML signal with «SDU» stereotype
SDULink types connectors between SAP and SAPClient ports
  Represented as Association Blocks so internal structure and behavior can be added at need in the concrete protocol
  Also note «SDULink» stereotype should be applied
  Provides mechanism to assert compatibility between these interface types between protocol entities of different protocols
Specific protocols defined in user models will specialize each of these elements and apply the appropriate stereotypes for the pattern

## Slide 17: Stereotypes – Protocol Entity
All ProtocolEntity blocks should have that stereotype applied
All protocol state machines of a protocol entity should have that stereotype applied.
The above statements are true even when specializing the library elements shown earlier

## Slide 18: Stereotypes – Ports
All ports and interfaces should have appropriate stereotype applied
Note separate stereotypes for ports vs interfaces
The above statements are true even when specializing the library elements shown earlier

## Slide 19: Stereotypes – Connections and Flows
All model elements using the pattern should have appropriate stereotype applied
  Even when specializing the library elements shown earlier
Note the same stereotypes for association and connector

## Slide 20: Stereotypes – Complete Set
Reminders
  These stereotypes are applied to mark the aspects of the Layered Comms pattern aspect being used
  Assists in human readability and tool support for creation and tool checking/queries
  Remember to apply the appropriate stereotypes in user models, even when using specialization from the supplied library elements

## Slide 21: Layered Comms Protocol Definition “Pre-Fab”
Available to bootstrap a user model package that defines a protocol model.
Copy from the profile library; Paste into the user model; Rename things; Augment

## Slide 22: The Protocol Model Pre-Fab
Defining a protocol using the Layered Comms profile has many aspects
The _Prefab_ProtoX_Protocol package is a good starting point to assist in that task
  To get started, copy that package and paste into your user model and rename it according to the protocol to be defined
ProtoX is the name of the protocol
Library elements from the profile are specialized (with applied stereotypes) for the ProtoX protocol
Recommended diagrams are also present
The package named To Be Renamed is a smart package having the elements that need to be renamed (find&replace “protox” with your protocol name).
  Afterwards, delete the To Be Renamed package.

## Slide 23: ProtoX from the Pre-Fab – PDU Aspects
Specific protocol elements already specialize profile model elements
Stereotypes are already applied

## Slide 24: ProtoX from the Pre-Fab – SDU Aspects
Specific protocol elements already specialize profile model elements
Stereotypes are already applied

## Slide 25: ProtoX from the Pre-Fab: All

## Slide 26: Example: Using Already-Define Protocols to Model Two Hosts Communicating with a Layered Protocol Stack
com.meadortech.ExampleLayeredComms001.mdzip

## Slide 27: Example Layered Comms Stack
nn2 : NetNode
nn1 : NetNode
Datagram PE
Datagram PE
Network PE
Network PE
Datalink PE
Datalink PE
SAP
SAP
SAP
SAP
SAP
SAP
SAP
SDUs
SDUs
SDUs
SDUs
PDU Link
PDU Link
PDU Link
PDUs
PDUs
PDUs
SDU Link
SDU Link
SDU Link
SDU Link
PDU Ports
Two network nodes participate in a layered comms relationship.
The Datagram protocol is over the Network protocol, which is over the Datalink protocol.

## Slide 28: Layered Interconnections
Layered Comms Black Box View
3 protocols
Each protocol
  PDU Ports
  PDU Link Connector
  PDU Item Flows
Layering of connectors noted using the “Over” stereotype

## Slide 29: Layered Protocol Entities within Network Node
Parent Block with optionality on PDU ports
  Binding connectors between inner/outer PDU Ports
Layered protocol entities within the NetworkNode
  SAP Ports
  SAP Clients
  SDU Link connectors
  SDU item flows not shown

## Slide 30: SystemX White Box Layered Comms

## Slide 31: Related Work
Inspired by…
  SysML v2 LayeredComms library https://github.com/guymeador/usm
  Open-licensed repository
  “Useful System Models”
README
  From the repository above
  Applies to the SysML v2 library for LayeredComms and other work on DataFields, too.
SysML v1 MDZIP to be available
  The profile and example provided in this presentation will also be available at the above link.
  Download and open to explore the profile and example more deeply
  Use it to impress your friends!
  Provide feedback to make it better!
Thank you to the OMG System Modeling Community User WG’s Layered Interface Pattern subgroup members listed below. Your perspectives, wise counsel, feedback, advice, review, discussion, and patience have made this work all the better!
  Sanford Friedenthal
  Hans Peter de Koning
  Andrew Muxen
  Austin Roberts
  Peter Shames
Separate feedback was also received from others listed here. Thank you!:
  Vince Molnar
  Juozas Vaicenavicius
  Simas Vaitekicius
Other Resources
2015-2016 Original INCOSE papers and model
  Peter M. Shames, Marc A. Sarrel, Sanford Friedenthal
    http://www.omgsysml.org/A_modeling_pattern_for_layered_system_interfaces-INCOSE%20IS15_presentation-sarrel-shames.pdf
    http://www.omgsysml.org/A_modeling_pattern_for_layered_system_interfaces-INCOSE%20IS15_paper-sarrel-shames.pdf
    http://www.omgsysml.org/INCOSE_IS_2016_paper_Application-of-a-Layered-Interface-Modeling-Pattern.pdf
OMG System Modeling Community (Please join to participate)
  Systems Modeling Community | Object Management Group
  Users Working Group
    Layered Interface Pattern Working Group
      Advanced the examples from the above papers using SysML 2
      Updates to the original SysML v1 model from the above papers to express in SysML v2
      Other related papers and information available in the OMG SMC